PRODUCT NAME:

Trade Name:	BWT-900 DESCALER II

SECTION 1: HAZARDOUS INGREDIENTS / IDENITY INFORMATION

HAZARDOUS COMPONENT						TWA/TLV

HYDROCHLORIC ACID							5 PPM CEILING		(CAS # 7647-01-0)

SECTION 2: PHYSICAL / CHEMICAL CHARACTERISTICS

Boiling Point:  1820 F				Specific Gravity (H2o =1): 1.12

Vapor Pressure (mm Hg): N/A			Melting Point: N/A

Vapor Density (Air =1):	 1.27			Evaporation Rate (Butyl =1):  1

Solubility in Water: COMPLETELY SOLUBLE

Appearance and Odor: COLORLESS TO LIGHT YELLOW FUMING LIQUID WITH  PUNGENT ODOR.

## SECTION 3: FIRE AND EXPLOSION HAZARD DATA

Flash Point: (Method):	Not considered a fire hazard.

Flammability Limits: LEL:  N/A		UEL:  N/A

Extinguishing Media:

Select media suitable for surrounding fire.  Use water spray to cool drums.

Special Fire Fighting Procedures:

Fire fighting procedures: Wear full protective clothing and NIOSH approved self contained breathing apparatus with full facepiece operated in the pressure demand or other positive pressure mode.  Structural firefighter’s protective clothing may be ineffective for fires involving hydrochloric acid.  Stay away from the end of tanks.  See unusual fire and explosion hazards.

.

Unusual Fire Explosion Hazards:

Fire and explosion hazard releases hydrogen chlorine gas when heated.  Flammable and potentially explosive hydrogen gas can be generated inside metal drums and storage tanks.  Product will react with most organic materials with the evolution of heat and large quantities of dense, white fumes.

### NFPA Hazard Rating:	Health:	3	Fire:	0	Reactivity:	2 	Special:  acid

SECTION 4 – REACTIVITY DATA

Stability:  STABLE

Incompatibility:

Most metals, alkalis, metallic oxides, amides, strong oxidants including fluorine; vinyl acetate, propiolactone (BETA).  Propylene oxide.   Also water reactive materials such as concentrated sulfuric acid, oleum and acetic hydride.  Also carbonates, cyanide, and sulfides in contact with this acid liberate toxic gases.

Hazardous Polymerization:

Will not occur.

Hazardous Decomposition Products:

HCL evolution accelerated by heating or contact with water reactive material.

SECTION 5: HEALTH HAZARDS

Routes of Entry: Inhalation:    YES		Skin and Eyes:  YES		Ingestion:  YES

Inhalation:

Inhalation of excessive concentrations of vapor immediately produces severe irritation of the upper respiratory tract, resulting in coughing, burning of the throat, and a choking sensation.

Eye Contact:

Vapor or solution rapidly causes severe irritation of the eyes and eyelids.  If not removed by thorough irrigation with water, there may be prolonged or permanent visual impairment or total loss of sight.

Skin Contact:

Contact causes severe burns unless immediately washed off.  Repeated contact with dilute solutions may lead to dermatitis.  Exposure to the concentrated vapor my result in burns or dermatitis.

Ingestion:

If swallowed, causes severe burns of the mucous membranes of the mouth, esophagus and stomach.

First Aid:

Eye Contact:

Immediately flush with water for 15 minutes while holding eyelids open.  Do not use chemical antidotes.  Speed is essential.  Call a physician.

Skin Contact:

Immediately flush with water for at least 15 minutes, while removing contaminated clothing and shoes.  Do not use chemical antidotes.  Wash clothing before re-use, destroy contaminated shoes.  Call a physician.  Speed is essential.

SECTION 5: HEALTH HAZARDS CONT’D

Inhalation:

Remove to fresh air.  If breathing is difficult give oxygen.  If breathing has stopped, give artificial respiration, preferably mouth to mouth.

Ingestion:

DO NOT INDUCE VOMITING!   Drink large amounts of water, milk or preferably a non-gassing

neutralizer such as milk of magnesia.  Do not give carbonates, bicarbonates of chalk.

Notes to physician:

This material is corrosive to the intestinal tract.  If swallowed, gastric lavage should be used with extreme caution.

Chemicals listed as Carcinogen by:

OSHA:					NO

I.A.R.C. MONOGRAPHS:		NO

NATIONAL TOXICOLOGY PROGRAM:	NO

SECTION 6: SPECIAL PROTECTION INFORMATION

Ventilation type:

A system of local and/or general exhaust is recommended to keep employee exposures below the airborne exposure limits.

Respiratory Protection:

For atmospheric concentration above PEL/TLV and up to 50 PPM use a self-contained breathing apparatus.

Skin Protection:

Gloves preferably neoprene or NBR

Eye Protection:

Splash goggles and face shield

Other Equipment:

Acid resistant apron

Additional Protective Measures:

Wash facilities and eye wash station should be available.

SECTION 7: SPECIAL PRECAUTIONS AND SPILL/LEAK PROCEDURE

Handling and Storage:

Store closed containers in clean, cool, open or well ventilated areas.  Keep out of sun.  Use non-sparking tools and prohibit smoking in area around tank and pipes where hydrogen might be generated.

Spill and Leak Procedure:

Keep people away.  Shut off or extinguish all sources of ignition.  Keep upwind.  Shut off leak if without risk.   If necessary to enter spill area, wear self-contained breathing apparatus and full protective clothing including boots.  Dike with sand or earth and pump into salvage tank.  Flush spill area with water and neutralize with lime or soda ash.  Run-off to sewers may create health and explosion hazards; notify fire and health control authorities.  Keep out watersheds and waterways.  If not possible, notify pollution control authorities.

Waste Disposal:

Flush large spills with water to holding area and neutralize with soda ash or lime.  Follow local, state and federal regulations.

SECTION 8 - REGULATORY INFORMATION

Proper Shipping Name:  	CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. (HYDROCHLORIC 				ACID)

Hazard Class: 			8

Packing Group			PG II

ID Number:			UN3264

Label Requirements:		CORROSIVE

# Section 313 Supplier Notification:

This product contains the following toxic chemicals subject to reporting requirements of Section 313 of the emergency planning and community right to know act of 1986 and of 40 CFR 372:

HYDROCHLORIC ACID

# Date prepared: 10/01/01

The seller makes no warranty expressed or implied concerning the accuracy or any results to be obtained from the  use of any information and no warranty expressed or implied concerning the use of the products.  The buyer assumes all risks of the use and/or handling.

END OF FORM