Shanghai Senda Fancywood Industry Co

229 XI TAI ROAD, SHANGHAI, CHINA, 200232

TEL.86-21-5436-5561 FAX. 86-21-5436-0331

# MATERIAL SAFETY DATA SHEET

PRODUCT IDENTIFICATION:       	Hardwood Plywood

(Urea-Formaldehyde Bonded)*

SYNONYMS:                      	None

TRADE NAME:                     	Fancy Plywood

GRADING:	HPVA  HP-1-1994

DESCRIPTION

This panel product contains a hardwood veneer face (occasionally a decorative softwood face) bonded to

wood components such as other wood veneer, particleboard, or medium density fiberboard (MDF) using

urea-formaldehyde resin.

POTENTIAL AIRBORNE RELEASES

The product may release very small quantities of formaldehyde (CAS No. 50-00-0) in gaseous form.

Emissions decrease through time as the panels age. Manual or mechanical cutting or abrasion processes

performed on the product can result in generation of wood dust.

PHYSICAL DATA

Boiling Point……………………..…… 	Not applicable

Specific Gravity (H2O = 1)……………	< 0.60

Vapor Density………………………...	Not applicable

% Volatiles By Vol……………………   	0

Melting Point…………………………    	Not applicable

Vapor Pressure……………………… .   	Not applicable

Solubility in H2O (% by wt.)…………   	< 0.1%

Evaporation Rate (Butyl Acetate = 1)…    	Not applicable

PH…………………………………….     	Not applicable

Appearance and Odor…………………           	Light to dark color. Color and odor

are dependent upon wood species.

*This fact sheet is for products that have not been finished (coated, laminated, or overlaid) or treated

(for example, with preservative or fire retardant).

FIRE AND EXPLOSION DATA

Flash point……………………………           	Not applicable

Autoignition Temperature……………                        Not available (will depend upon duration of exposure to

heat source and other variables)

Explosive Limits in Air………………                        See below under "Unusual Fire and Explosion Hazards"

Extinguishing Media………………….           	Water, Carbon dioxide, Sand

Special Fire Fighting Procedures…….                        None

Unusual Fire and Explosion

Hazards………………………………            	Sawing, sanding or machining can produce wood dust as

a by-product which may present an explosion hazard if a

dust cloud contacts an ignition source. An airborne

concentration of 40 grams of dust per cubic meter of air

is often used as the LEL for wood dust.

REACTIVITY DATA

Conditions Contributing to

Instability……………………………            	Stable under normal conditions.

Incompatibility………………………         	Avoid contact with oxidizing agents. Avoid open flame.

Product may ignite in excess of 4000F.

Hazardous Decomposition

Products………………….…………             	Thermal and/or thermal oxidative decomposition can

produce irritating and toxic fumes and gases, including

carbon monoxide, hydrogen cyanide, aldehydes, organic

acids and polynuclear aromatic compounds.

Hazardous Polymerization………….          	Not applicable

HEALTH EFFECTS INFORMATION

Exposure Limits:

Formaldehyde………………………           	OSHA PEL - TWA      	0.335 ppm

OSHA PEL - STEL     	0.335 ppm

ACGIH TLV - CEILING  	0.335 ppm

Wood Dust (all soft and hard

Woods except Western red cedar)…	OSHA PEL - TWA     5mg/m3

OSHA PEL - STEL    10mg/m3

Wood Dust (Western red cedar)…….                          OSHA PEL - TWA     2.5mg/m3

Wood Dust (Softwood)………………          	ACGIH TLV - TWA    5mg/m3

Wood Dust (certain hardwoods such

as beech and oak) ……………………       	ACGIH TLV - TWA    1mg/m3

Eye Contact…………………………         	Gaseous formaldehyde may cause temporary irritation or

a burning sensation. Wood dust can cause mechanical

irritation.

Skin Contact…………………………            	Both formaldehyde and various species of wood dust

may evoke allergic contact dermatitis in sensitized

individuals.

Ingestion……………………………..           	Not likely to occur.

Inhalation:

Gaseous formaldehyde……………….        	May cause temporary irritation to eyes, nose and throat.

Some reports suggest that formaldehyde may cause

respiratory sensitization, such as asthma, and that pre-

existing respiratory disorders may be aggravated by

exposure.

Formaldehyde is listed by the International Agency for

Research on Cancer (IARC) as a probable human

carcinogen. The National Toxicology Program (NTP)

includes formaldehyde in the Annual Report on

Carcinogens. Formaldehyde is regulated by OSHA as a

potential cancer agent.

In studies involving rats, formaldehyde has been shown

to cause nasal cancer after long-term exposure to very

high concentrations (14+ ppm), far above those

normally found in the workplace using this product.

The National Cancer Institute (NCI) conducted an

epidemiological study of industrial workers exposed to

formaldehyde (published June 1986). The NCI

concluded that the data provides little evidence that

mortality from cancer is associated with formaldehyde

exposure at the levels experienced by workers in the

study.

Wood Dust……………………………           	May cause nasal dryness, irritation and obstruction.

Coughing, wheezing, and sneezing; sinusitis and

prolonged colds have also been reported.

Depending on species, may cause respiratory

sensitization and/or irritation. Prolonged exposure to

wood dust has been reported by some observers to be

associated with nasal cancer. Wood dust is not listed as

a carcinogen by IARC,NTP or OSHA.

PRECAUTIONS, SAFE HANDLING

Formaldehyde:  Provide adequate ventilation to reduce the possible buildup of formaldehyde gas,

particularly when high temperatures occur.

Wood Dust:  Avoid dusty conditions and provide good ventilation.

GENERALLY APPLICABLE CONTROL MEASURES

Ventilation: Provide adequate general and local exhaust ventilation to keep airborne contaminant

concentration levels below the OSHA PELs.

Personal Protective Equipment: Wear goggles or safety glasses when manufacturing or machining the

product. Wear NIOSH/MSHA approved respirator when the allowable exposure limits may be

exceeded. Other protective equipment such as gloves and outer garments may-be needed depending on

dust conditions.

EMERGENCY AND FIRST AID PROCEDURES

Eyes………………………………….             	Flush eyes with large amounts of water. Remove to

fresh air. If irritation persists, get medical attention.

Skin…………………………….……                             Wash affected areas with soap and water. Get medical

advice if rash or persistent irritation or dermatitis

occurs.

Inhalation…….………………….….              	   Remove to fresh air. Get medical advice if persistent

Irritation, severe coughing or breathing difficulty

occurs.

Ingestion……………………………              	 Not applicable

Manufacturer Name and          Effective Date         Supersedes Date     Prepared BY

Address

Shanghai Senda Fancywood      Feb. 27, 2006                            Jerry Wong

Industry Co.

229, Xi Tai Road Shanghai

China 200232

Tel: 0086-21-54365561

Fax: 0086-21-54360331

IMPORTANT:  The information and data herein are believed to be accurate and have been compiled

from sources believed to be reliable. It is offered for your consideration, investigation and verification.

The National Forest Products Association (NFPA) makes no warranty of any kind, express or implied,

concerning the accuracy or completeness of the information and data herein. NFPA will not be liable

for claims relating to any party's use of or reliance on information and data contained herein regardless

of whether it is claimed that the information and data are inaccurate, incomplete or otherwise

misleading. It is incumbent upon the user to obtain the most up-to-date information.