MATERIAL SAFETY DATA SHEET

### Product identify :  WOD-702

## 1. MANUFACTURER INFORMATION :

Supplier : SUMEI CHEMICAL CO., LTD.

Address : NO. 20, Lin 6, Fu Lin Vallage, Kuan Yin Hsiang, Taoyuan, Taiwan, R.O.C.

Tel    : 886-3-4839311          Fax : 886-3-4839317

Emergency Phone : Local Emergency.

## 2. COMPOSITION / INFORMATION INGREDIENTS:

| Hazardous Components | Chemical Fomula | % By Wt. | CAS NO. | STEL | TWA |
| --- | --- | --- | --- | --- | --- |
| 1.6-hexanediol diacrylate |  | 15 | NIL | NIL | NIL |
| Tri-propyleneglycol diacrylate |  | 37 | NIL | NIL | NIL |
| Tri-methylolpropane triacrylate |  | 32 | NIL | NIL | NIL |

## 3. PHYSICAL/CHEMICAL CHARACTERISTICS:

Appearance : Pale white liquid                Odor: slight acrylate monomer-like

Boiling point : nil                           Vapor Density: <1 ( Air= 1)

Vapor pressure : <0.1 mmHg                  Specific Gravity: 1.05 ~ 1.15

Evaporation Rate : nil                        pH Value : nil

Solubility in water : Insoluble.

## 4. FIRE AND EXPLOSION HAZARD DATA :

Flash Point ( Test Method ) : >200℉ (Open Cup )

Flammable Limits : nil (LEL)   nil(UEL)

Extinguishing Media : Carbon Dioxide, Foam, Dry Chemical and Water Fog.

Special Fire Fighting Procedures: Use water spray to cool fire exposed surfaces and to

protect personnel. Shut off “fuel” to fire. If a leak or spill has not igaited, use water spray

to disperse the vapors and protect men attempting to stop a leak. Either allow fire to burn

under controlled conditions or extinguish with alcohol type foam or dry chemical Try to

cover liquid spills with foam. Firefighters must use self-contained breathing apparatus

## 5. REACTIVITY DATA :

Stability :  Unstable.      Condition to avoid : Heat, light.

Hazardous Polymerzation : May occur. Material to avoid : peroxide

Hazardous Decomposition products : nil.

## 6. HEALTH INFORMATION AND PROTECTION:

Methods get into body: Inhalation, Contact, Ingestion.

Nature of hazard:

Eye Contact : Irritating, and will injure eye tissue if not removed promptly.

Skin Contact: Frequent or prolonged contact may defat and dry the skin.

Inhalation : Vapor concentrations above recommended exposure level may be irritating

to the eyes and the respiratory. May cause headaches, dizziness, anesthesia,

drowsiness, central nervous system effects..

Ingestion : Small amounts of the liquid aspirated into respiratory system during ingestion

or from vomiting may cause bronchitis or pulmonary edema.

Emergency & First Aid ：

Eye Contact：

Flush with plenty of water for at least 15 minutes and seek medical attention.

Skin Contact：

Remove contaminated clothing and wash contact area with soap and water for 15 minutes. Particular attention should be paid to hair, nose, ears and other areas not easily cleaned.

Ingestion：

If appreciable quantities are swallowed, seek medical attention.

Inhalation：

In case of exposure to a high concentration of vapor or mist, remove to fresh air. If breathing has stopped, administer artificial respiration and seek medical attention.

## 7. EXPOSURE PRECAUTION:

Personal Protection :

Eye/Face protection : Chemical-type goggles or face shield are recommended

Skin protection : Protective clothing, Safe shoes, Rubber Or Plastic gloves must be worn.

Breath protection : Use approved respirator

Ventilation Device：

Local Exhaust - Recommended to control exposure which may result from operations generating aerosols and hot operations generating vapors.

Mechanical - Not commended to control exposure for operations generating aerosols and vapors.

Caution for Storage and Handling :

Avoid to light, and prevent to exposure in extremely temperature(<30℃).

## 8. SPILL OR LEAK AND WASTE TREMENT:

Spill or Leak Procedures: The spills can be taken with sand or other inert absorbent, then recover

into container as Waste.

Waste management:

Wasted Container must pull out all content and clean by water.

Waste Content must incinerate in compliance with applicable laws and regulations.

## 9. TRANSPORT INFORMATION:

| UN NO. | Nil | Danger classify | Nil | Hazard Labels | Nil |
| --- | --- | --- | --- | --- | --- |